## Slide 1: MEG実験 陽電子スペクトロメータの 性能と今後の展望
Yuki Fujii
On behalf of the MEG collaboration
JPS meeting @ Hirosaki University
17th Sep. 2011

## Slide 2: Outline
Introduction
Run 2009 & 2010
Status of run 2011
Noise reduction
Summary and prospects

## Slide 3: Introduction
The decay of μeγ is strictly forbidden in the standard model because of lepton flavor conservation
BUT… some of beyond the SM (e.g. SUSY) predict this decay can happen in the range of 10-11-10-15
  Previous upper limit is 1.2x10-11 (MEGA experiment)
  μeγ is a good probe to search for new physics !
Background
  Radiative decay (prompt)
  Michel decay + γ (accidental)
Experimental requirement
  High resolution detector  reduce background
  Operation under high luminosity  high statistics
μ
e
γ
signal
μ
e
γ
ν
ν
prompt
?
μ
e
γ
ν
ν
accidental
dominant

## Slide 4: Introduction
The MEG experiment started to search for μeγ in 2008
  World’s most intense DC μ+ beam @ PSI
  900 litter large Xenon calorimeter  (白:17pSE2, 金子:17pSE3)
  The COBRA (COnstant Bending RAdius) spectrometer  main topic
Result 2009 & 2010 : Br(μeγ) < 2.4x10-12 (90 % C.L.)
  5 times lower than previous one
   (大谷:18aSJ4, 岩本:19aSD7, 澤田:19aSD8)
Our sensitivity goal is a few × 10-13
  Performance improvement is essential !

## Slide 5: Introduction
The COBRA spectrometer
  COBRA magnet : fast sweeping low momentum e+ and get uniform angular response for signal e+
  Drift chamber : e+ tracking, low mass materials to reduce the production of background gamma ray
    Vernier pattern method
    Waveform data acquisition
  Timing counter : e+ timing, bar counters (φ measuring) + fiber counters (z measuring)

## Slide 6: Introduction
The COBRA spectrometer
  COBRA magnet : fast sweeping low momentum e+ and get uniform angular response for signal e+
  Drift chamber : e+ tracking, low mass materials to reduce the production of background gamma ray
    Vernier pattern method
    Waveform data acquisition
  Timing counter : e+ timing, bar counters (φ measuring) + fiber counters (z measuring)

## Slide 7: Introduction
The COBRA spectrometer
  COBRA magnet : fast sweeping low momentum e+ and get uniform angular response for signal e+
  Drift chamber : e+ tracking, low mass materials to reduce the production of background gamma ray
    Vernier pattern method
    Waveform data acquisition
  Timing counter : e+ timing, bar counters (φ measuring) + fiber counters (z measuring)

## Slide 8: Introduction
Positron measurement
  Coordinate system
  Hit reconstruction
    R  time reading edge
    Z  charge division w/ Vernier pad
  Track reconstruction
    Kalman filter
e+
θ
◉
e+
z
(Beam axis)
z
x
φ
y
R

## Slide 9: Run 2009 & 2010
Run and analysis summary of 2009 and 2010
Drift chamber alignment
   Millipede using cosmic rays
COBRA Magnetic field
   reconstructed field
  Bφ and Br are corrected a possible misalignment of hole probe to conserve the Maxwell’s equations from measured Bz
All APDs off because of noise problem
Drift chamber waveform in 2010 was a little noisier than in 2009 (σ of pedestal : ~1.8 mV  ~2.0 mV)

## Slide 10: Run 2009 & 2010
Performance estimation
  Momentum resolution : Michel edge fitting and double turn events
  Angular & vertex resolutions : Double turn events
  Efficiency : count #of MD
  Correlations : sideband data
Here
μ
e
ν
ν
Michel

## Slide 11: Run 2009 & 2010
All performance of the e+ spectrometer are estimated by data itself (radiative decay events, Michel decay events, and so on)
 | 2009 | 2010
Ee | 330 keV (core 82 %) | 330 keV (core 79 %)
φ (at φ=0) | 6.7 mrad | 7.2 mrad
θ | 9.4 mrad | 11.0 mrad
Z | 0.15 cm | 0.20 cm
Y | 0.11 cm (core 87 %) | 0.11 cm (core 85 %)
Teγ (RMD) | 150 psec | 130 psec
εMichel | 40 % | 34 %

## Slide 12: Run 2009 & 2010
All performance of the e+ spectrometer are estimated by data itself (radiative decay events, Michel decay events, and so on)
 | 2009 | 2010
Ee | 330 keV (core 82 %) | 330 keV (core 79 %)
φ (at φ=0) | 6.7 mrad | 7.2 mrad
θ | 9.4 mrad | 11.0 mrad
Z | 0.15 cm | 0.20 cm
Y | 0.11 cm (core 87 %) | 0.11 cm (core 85 %)
Teγ (RMD) | 150 psec | 130 psec
εMichel | 40 % | 34 %
Noise
+
increased dead channels
Increased dead channels
Better DRS clock

## Slide 13: Status of 2011
7 drift chamber modules were replaced because of increased remaining current or frequent trip
Physics data taking started at the end of June
In 2009 and 2010, only 14 MHz noise is dominant
 reduced by adjusting charge integration time
  other noise components appeared (>30 MHz from APD fiber counters)
Working of hardware noise reduction was done in the middle of July
  Change HV module for drift chambers and turn off noisy APD channels
April | May | June | July | Aug. | Sep.
Detector installation
Calibration
Detector check
Physics run
CEX
14 MHz

## Slide 14: Status of 2011
At the beginning of 2011 run, noise situation was the worst…
But

## Slide 15: Status of 2011
At the beginning of 2011 run, noise situation was the worst…
After hardware modifications, the lowest noise condition realized !
The APD fiber counters are partially operational now (not all)
  Data quality to be checked

## Slide 16: Noise reduction
Performance of noisy runs and low noise runs
  compare 2 condition by checking single hit resolutions (residuals between reconstructed wire hit and reconstructed track)
  Single hit resolutions are estimated from double Gaussian fitting
Give up noisy data to improve ?  OF COURSE NO !
Filtering
  Low pass filter  small contribution
  High pass filter  distort the shape of signal pulse
  FFT
 | 2010 | 2011 (noisy) | 2011 (low noise)
Intrinsic Z (um) | 668 (core 56 %) | 758 (core 52 %) | 710 (core 56 %)
Intrinsic R (um) | 209 (core 66 %) | 233 (core 66 %) | 197 (core 67 %)
~ 1 month data taking

## Slide 17: Noise reduction
Large periodical noises are eliminated in FFT power spectrum from DCH waveform
After that, filtered spectrum is transformed inverse to the waveform
  Charge integration done for filtered waveform
FFT

## Slide 18: Noise reduction
inverse
Large periodical noises are eliminated in FFT power spectrum from DCH waveform
After that, filtered spectrum is transformed inverse to the waveform
  Charge integration done for filtered waveform

## Slide 19: Noise reduction
Thanks to offline noise filtering, twice better σ of pedestal realized (2.4 mV1.2 mV)

## Slide 20: Noise reduction
Thanks to offline noise filtering, twice better σ of pedestal realized (2.4 mV1.2 mV)
Single hit Z resolution improved !!
  758  664 um, #of hits increased

## Slide 21: Noise reduction
Thanks to offline noise filtering, twice better σ of pedestal realized (2.4 mV1.2 mV)
Single hit Z resolution improved !!
  758  664 um, #of hits increased
Efficiency & resolutions
  Very good !
Ep
φ
θ
432 keV (80 %)
 380 keV (79 %)
11.7 mrad (68 %)
 12.4 mrad (78 %)
13.1 mrad
 11.6 mrad

## Slide 22: Noise reduction
Filtering for waveform in low noise condition
  What happen if FFT filtering used in low noise condition ?
  Single hit Z resolution
    Only a few % better (710  697 um)
    #of hits increased
  Efficiency and resolutions improved, too
14.4 mrad (84 %)
 11.4 mrad (76 %)
12.0 mrad
 11.7 mrad
390 keV (82 %)
 321 keV (75 %)
Ep
φ
θ

## Slide 23: Performance summary
2011 performance summary (Preliminary)
  Only parts of data were analyzed
  Correction for resolutions in 2011 not yet done
  Calibrations still ongoing
 | 2010 | 2011 noisy | 2011 low noise
Intrinsic Z (um) | 668 (core 56 %) | 664 (core 57 %) | 697 (core 56 %)
Intrinsic R (um) | 209 (core 66 %) | 237 (core 65 %) | 201 (core 68 %)
Ee (keV) | 330 (core 79 %) | 380 (core 79 %) | 321 (core 75 %)
φ (mrad) | 7.2 (core, φ=0) | 12.4 (core 78 %) | 11.4 (core 76 %)
θ (mrad) | 11.0 | 11.6 | 11.7
#of 2 turn e+ | - | 2499  4019 | 3184  3833
Preliminary !

## Slide 24: Summary and prospects
Summary
  Thanks to FFT noise filtering, data quality of noisy runs achieved to the level of low noise situation !
    Further check needed
      Transformation accuracy
      Check with more data
      Single hit R resolution
Prospects
  Calibrations for the spectrometer in preparation now
    Better resolutions and efficiency expected
  Monochromatic calibration source for the spectrometer
    Mott scattering with e+ beam (energy tunable)
  Hardware improvement for εe (≒ reduce materials between DC and TC)
    Readout cable exchange to thinner one (40 %  50 + x %)
    According to changing cables, the support structure system for drift chambers will be updated
current
Future candidate

## Slide 25: backup

## Slide 26: Vernier method
Vernier α is defined as
where
Compare α to reconstructed z position, we can decide z more precisely
wire z
Vernier α

## Slide 27: Positron correlations
Correlations
true
reconstructed
Case : Emeas < Etrue
Ymeas < Ytrue
φmeas > φtrue
…

## Slide 28: Efficiency
Material between drift chambers and timing counters make lower efficiency because of multiple scattering
Chart: 
| frame | cable | preamp | duct
Breakdown of Inefficiency caused by DC components | 49 | 28 | 19 | 4

## Slide 29: Check for APD data
Quality check for APD outputs
First step
  Matching between hit z at fiber and e+ track at timing counter bars
  Only downstream of APDs are working now
z
e+
MC

## Slide 30: Check for APD data
Quality check for APD outputs
First step
  Matching between hit z at fiber and e+ track at timing counter bars  peak position is same, but large tail found
  Only downstream of APDs are working now
z
e+
MC
Data
ー DS
ー US
Multiple scattering ?