## Slide 1: SiPMを用いたシンチレーションカウンターによる 細分化ポジトロン時間測定器のビーム試験結果
西村美紀 (東大)
内山雄祐（素セ）、大谷航（素セ）、
M. de Gerone（Genova Univ.）、Flavio Gatti(Genova Univ.)、調翔平（九大）
他 ＭＥＧコラボレーション
日本物理学会 2013年秋季大会
高知大学

## Slide 2: μ → eγ
Search for charged lepton flavor violation (cLFV), μ eγ
  Forbidden in the SM
  Many BSM predict large branching ratios
Current best upper limit set by MEG:
90% C.L. (Phys. Rev. Lett. 110(2013) 201801)
upgrade
at rest
Signal
52.8MeV
Back-to-back
Time coincidence
Physics BG
(radiative muon decay)
<52.8MeV
Any angle
Time coincidence
Accidental BG
<52.8MeV
Any angle
Random
Dominant

## Slide 3
µ
γ
e
液体キセノンガンマ線検出器
立体交差ワイヤーポジトロン飛跡検出器
細分型ポジトロン時間測定器
upgrade
(detail of MEG upgrade; arXiv:1301.7225)

## Slide 4: Pixelated Timing Counter for MEG upgrade
upgrade
3 SiPMs
series connection
Plastic
scintillator
PCB
present
For good time resolution
Pixelated TC is employed.
90 mm
40
5
a higher level of segmentation
  Using multiple hit time
  Flexible detector layout
small counter with SiPM
  A good timing resolution
  Less pileup
PMT
Scintillator
~250 counters (upstream, downstream side)

## Slide 5
MC simulation
5-8 counter hit
Signal positron
Average # of hit
6.6
Number of hit counters (MC)

## Slide 6: Multiple hit scheme
Requirement
Good single counter resolution
Single counter R&D (Uchiyama’s talk)
smaller counter
Hit many counters
optimization counter assembly with MC
larger counter
30-40 ps
~5ps
Resolution vs. # of hit counters (MC)
Resolution (psec)
Overall timing counter resolution is

## Slide 7: Multiple hit scheme
Resolution vs. # of hit counters (MC)
Resolution (psec)
30-40 ps
~5ps
Overall timing counter resolution is
⇒ the average time resolution :
30-35 ps (current ~76 ps)
~70 ps
90x40x5 mm scintillator
Average # of hit
6.6
Number of hit counters (MC)

## Slide 8: R&D plan
Single counter R&D
  Make prototype
  Basic characteristics
  Counter geometry optimization
Timing counter layout study
  Size optimization with MC
  Optimize counter layout
Multi counter prototype
  Prove multiple hit scheme by beam test
  Electronics test
  Calibration R&D
Construct
Uchiyama’s talk
done

## Slide 9: Counter Size Optimization
Average number of hit increase with taller counter.
Single counter resolution is better with lower counter.
Chart: 
| 3 | 4 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Average # of Hit Pixel | 4.4 | 5.8 | 5.8 | 6.9 | 7.4 | 7.6 | 7.7 | 7.8 | 7.8
Counter height (cm)
Average # of hit counters (MC)
Chart: 
| 4 | 5 | 6 | 7 | 8 | 9 | 10
expected | 5.4927e-11 | 6.0756e-11 | 6.6073e-11 | 7.0993e-11 | 7.5594e-11 | 7.993e-11 | 8.4043e-11
measured | 4.84e-11 | 5.366e-11
9
Single resolution at 1MeV
Counter height (cm)
3 SiPMs
series connection
Plastic
scintillator
PCB

## Slide 10: Counter Size Optimization
4 cm for positrons concentrating region.
5 cm for the other region.
4 cm
5 cm
beam
target
Signal positron

## Slide 11: Beam Test in Frascati
Linac
Collider DAFNE
BTF
Damping ring

## Slide 12: Beam test configuration
Beam
48 MeV Positrons (1-3/bunch), bunch width of 10 ns
Inside the black box
Counters (90x40x5 mm, BC418)
  8 counters with HAMAMATSU (S10943-2547(X), 3x3 mm2, 50μm-3600 pixels) SiPMs
  6 counters with AdvanSiD SiPMs
Reference counter (5x5x5 mm, BC422, 1 HAMAMATSU SiPM) for time reference & trigger
Lead-glass Calorimeter for monitoring the beam
Electronics
Long cable
6 DRS (digitizer)
1~3 e+
3 cm
Black box
Lead-glass Calorimeter
Counters
Reference counter
9.5 cm

## Slide 13
counters
Black box
Beam line
Reference counter
Magnet
Linac
Single counter

## Slide 14: DRS synchronization
Before
σ=377 ps
After
tch1-tch2
tch1-tch2
synchronize many different channels with common clock.
Time jitter among counters 23-26 ps

## Slide 15: DRS synchronization
synchronize many different channels with common clock.
Time jitter among counters 23-26 ps
Before
σ=377 ps
After
Sigma 26.3 ps
tch1-tch2
tch1-tch2

## Slide 16: Selection
1e+ beam
2e+
3e+
After cutting the 2 or more positrons events, Landau shape charge distribution is obtained.
Charge distribution of 1st counter
2e
3e
Cut
1e+
Select 1 positron events

## Slide 17: Single counter performance
Single counter resolution is consistent one with Sr source in the lab.
All counter have the similar resolution ~75 ps
tcounter -tref
Resolution (psec)
Counter #

## Slide 18: Multiple Scattering
e
resolution
~8mm
Reconstruct hit position by (; scintillation light speed)
Measurement with source
Beam spot size

## Slide 19: multiple counter resolution
tcounters -tref
(todd –teven)/2
-2.5 -2 -1.5 -1 -0.5 0 0.5
(ns)
we can obtain the resolution of 47.0 ps with 8 counters and reference counter.
-2.5 -2 -1.5 -1 -0.5 0 0.5
(ns)
From ( even counter average time - odd counter average time ), resolution with 8 counters of 27.5 ps can be obtained.

## Slide 20: Multiple hit resolution
Multiple hit scheme works.
We obtained the better resolution with 8 counters.
ref. analysis
Subtract reference resolution and DRS jitter which is not similar our experiment.

## Slide 21: SiPM comparison
HAMAMATSU: high PDE
AdvanSiD: stable with temperature
Jitter reduction from multiple hit does not depend on SiPM.
We must employ the counter which single resolution is better.

## Slide 22: Summary and Prospects
Pixelated TC is employed for MEG experiment upgrade
  5-8 hits pixels information gives good resolution of 30-35 ps.
Beam test with 8counters in Frascati.
  obtain better resolution of ~30 ps with 8 counter
  Multiple hit scheme is confirmed.
Prospect
2013 Counter assemble optimization
2014 Calibration R&D
2014 Construct

## Slide 23: Back up

## Slide 24: TOF pixel dependence(MC)
Time difference is ~5ps.
(without effect of support structure)
Time difference

## Slide 25: Single Pixel Study
Test Counter
  SiPM
    HAMAMATSU MPPC (S10362-33-050C, 3x3 mm2, 50μm-3600 pixels)
  Fast plastic scintillator
    90x30x5mm, BC422
  glued with optical grease (OKEN6262A)
Source Sr90 (<2.28MeV, β-ray)
Reference counter
  5×5×5 mm scintillator BC422
  Readout by a MPPC
  Trigger, Collimate
Waveform digitizer sampling (DRS developed at PSI) @5GSPS
Voltage amplifier developed by PSI (Gain~20, 600 MHz bandwidth)
Shaping with high-pass filter & pole-zero cancellation
Long cable (7.4m) before amplifier
KEITHLEY Pico ammeter for MPPC bias (HV), Bias 218V~222V (for series connection)
3 or 4 SiPMs
Series connection

## Slide 26: waveform
Parallel connection
Series connection
Before shaping
After shaping
  Capacitance is larger
  ->waveform wider
[ns]
-60
-120
0
[ns]
-60
-120
0
  Waveform is sharper.
  We can obtain good resolution.
0
100
200
300
[mV]
0
100
200
[mV]

## Slide 27: Series vs. parallel connection
Parallel
  We can’t apply bias voltage to each MPPC. We should choose MPPCs which have the same characteristic.
  Capacitance ↑
  -> waveform wider
Series
  Automatically bias voltage is adjusted.
  Waveform is sharper.
Series connection gives us better results.

## Slide 28: Analysis
Signal time is picked-off by Constant-Fraction method (~10%)
  very leading-edge is relevant to precise timing
e hit time is reconstructed by the average of times measured at the both ends
Resolution of test counter is evaluated from (t0 + t1)/2 – tref
Reconstruct hit position by (; scintillation light speed)
trise~1.7 ns
baseline restoration by the
pole-zero cancellation @ preamp

## Slide 29: Single Pixel R&D
Position scan
Optimization
  Size
    length(60-120mm), width(3.5-5 mm), height(30, 40 mm)
  Scintillators
    BC422, BC420, BC418
  Manufacture of SiPM
    HAMAMATSU, KETEK, AdvanSiD
  Reflector
    Aluminized Mylar, Teflon tape, 3M radiant mirror
Single Pixel R&D with source is almost done!!
We could obtain the satisfying result about single pixel.

## Slide 30: resolution
track length: 75 ps→ 11 ps
gamma side: 67 ps →76 ps
Timing counter: 76ps → 30-35ps
130 ps → 84 ps (35% ↓)
present
upgrade
COBRA
DC
TC

## Slide 31: Resolution and efficiencies for MEG upgrade

## Slide 32: Upgrade summary

## Slide 33: Manufacture of SiPM (Preliminary)
HAMAMATSU
HAMAMATSU SiPMs give us the best resolution.
KETEK
AdvanSiD
Best resolution ~ 58 ps
~ 65 ps
~ 75 ps

## Slide 34: Scintillator Type
Test BC418, 420, and 422 which is 90x40x5mm with 4MPPCs
Scintillator Type | Single Resolution (ps)
BC422 | 51.2
BC420 | 57.7
BC418 | 55.8
Properties of ultra-fast plastic scintillators from Saint-Gobain

## Slide 35: Waveform
signal ->
sine wave ->

## Slide 36: Size Optimization
Single resolution is worse with larger pixel.
However # of hit pixel increases with larger pixels.
3cm height
measured
MC

## Slide 37: Result of size optimization
Larger pixel is better.
(Effect of high rate is not included.)
better
MC

## Slide 38: Counter Height
Pixels; z 21-120
=> Change pixel height 3 cm – 5 cm
3 cm
4 cm
5 cm
Pixel height affects small z hit number.
=> It is good to change the counter height with z position.