## Slide 1: MEG II実験 液体キセノン検出器の建設状況
家城 佳
for the MEG II collaboration
物理学会第71回年次大会

## Slide 2: search
MEG
(金子19aAH3)
is the good probe for new physics.
MEG II will search for with 10 times better sensitivity!
e+
γ
μ+
μ+
e+
γ
BSM
(ex. SUSY)
New!

## Slide 3: MEG II experiment
Additional detector (RDC) to identify BG
中浦、岩井
19aAH-10,11
intensity 2 7x107μ/s
LXe γ detector
家城、小川22pAN-3,4
e+ drift chamber
& timing counter
吉田、西村、中尾
19pCA-1,2,3
γ
e+
2
all resolutions
efficiency
2
Physics data taking will start from 2017!
μ+ beam

## Slide 4: Liquid Xe detector upgrade
2inch PMT× 216
12x12mm2 MPPC × 4092
1m
inner face
upgrade!
(CG)
Granularity & uniformity will improve
 γ energy resolution & position resolution expected to improve by a factor of 2!
900l liquid Xe
12mm
VUV-light sensitive large area
MPPC is newly developed in
collaboration with Hamamatsu.
S10943-4372

## Slide 5: Detector construction status
Production
Installation
Commissioning
4092 MPPCs
186 PCBs for MPPCs
Feedthrough + cables
Modified PMT holders
Refrigerator
…
LXe liquefaction
Operation test
LXe purification
Commissioning run
now

2016 summer ~
Status report in this talk
Simulation study in the next talk

## Slide 6: All PCBs and MPPCs are ready
4092 MPPCs (+ spare)
186 PCBs (+ spare)
We mounted all the MPPCs on PCBs, and tested all the PCBs!
All of the MPPCs are already tested.

## Slide 7: 4092MPPCs on 186 PCBs!
33cm

## Slide 8: 4092MPPCs on 186 PCBs!
33cm
to be installed

## Slide 9: Mass test
LED1
LED0
Data taking with strong LED light @ T= 20 degrees
V=Vhama (operation voltage from spec. sheet, Vover~5V)
Waveform and charge were measured for all ch in every PCB.
Averaged waveforms
Charge vs. ch
MPPC mounting + test = ~15min/PCB
186 PCBs  ~47hours in total
reference ch
time [ns]
200
100
0
V [mV]
-100
-200
0 1 2 …
channel ID
Charge
1
0.9
0.8

## Slide 10: Bad PCB channels
Two bad channels were found on PCB, associated with damaged sockets.
200mV
20mV
Normal ch
Bad ch
Bad PCBs are replaced with spare.  All channels are good after replacement.
MPPC sockets

## Slide 11: Charge of all MPPCs
Vertical axis is charge normalized by charge of a MPPC in batch A.
Batch A
B
C
D
All channels are good.
Batch by batch difference possibly due to crosstalk & afterpulse.

## Slide 12: Waveforms of all MPPCs
Batch A
B
C
D
Waveform of 4092 MPPCs overlaid.
All channels are good.
 Ready for installation!

## Slide 13: Feedthrough & PMT holders
MPPC signal feed-through is being constructed.
PMT holders (with improve geometry) are ready to install.
first flange
PCB-based design
co-axial like signal line in PCB
installation test
drawing

## Slide 14: LXe refrigerator & purification
Additional GM refrigerator
will be placed far from cryostat to prevent from noise
external stage
for GM refrigerator
new pump
getter (purification)
pulse-tube
refrigerator
Upgraded cryogenics system is being constructed to cope with increased heat flow from 4000 MPPCs.
Sufficient power (430W @ 160K) of new GM refrigerator is confirmed.
liquefaction

## Slide 15: Summary
All of the MPPCs are assembled on PCBs and tested.
Two bad PCBs are found and replaced. After replacement, all the channels are good.
Feedthrough, PMT holders and the cryogenics are also being prepared.

## Slide 16: Backup

## Slide 17: 186 PCBs!

## Slide 18: Mounting MPPCs on PCB

## Slide 19: Setup for PCB+MPPC test
MPPC assembly area
DRS
(12 ch)
HV
LED pulser
LED1
LED0
PCB+MPPC
T=20 deg
reference ch
We measured the charge and waveform of the LED light.

## Slide 20: Stability of the LED and temperature
LED0
LED1
LED light and the temperature were stable over all period.
Charge of the reference MPPC was measured in all the runs.

## Slide 21: PCB ch dependence
The measured charge may depend on the PCB channel, due to the non-uniformity of the LED light and the imperfect calibration of electronics.
We checked this by putting #00004 at ch0~21.
LED0
LED1
PCB ch dependence is corrected in the analysis.

## Slide 22: Charge vs. serial
LED0 (PCB ch0~10)
LED1 (PCB ch11~21)
Systematic difference is seen for two LEDs.
Reference MPPC shows different behavior.

## Slide 23: Charge resolution
For each run, I selected two MPPCs and checked the resolution.
resolution = RMS of (charge of ch4 – charge of ch3) / (charge of ch4 + charge of ch3)
example of charge diff histogram
Resolution vs. serial no.
Batch by batch difference is small.

## Slide 24: Charge vs. HV
Batch A
B
C
D
Vhama
Vhama – 2V
Vhama + 2V
For batch C and D, charge increases much at higher V probably because the CTAP factor is large. (charge ∝ gain x CTAP )

## Slide 25: CTAP meas. in room temp
Batch A
B
C
D
CTAP probability is measured for some of the MPPCs in room temperature.

## Slide 26: Averaged waveforms
Batch A
B
C
D
Profile histograms for four batches. Error bar is RMS of each bin.

## Slide 27: All waveforms
Batch A
B
D
C

## Slide 28: Charge resolution vs. V
Batch A
B
D
C