## Slide 1: MEG II 実験液体キセノンガンマ線検出器における取得データサイズ削減手法の開発 Development of the data size reduction method for MEG II liquid xenon detector
小川真治、 他MEG IIコラボレーション
@日本物理学会 第72回年次大会
2017.03.19

## Slide 2: Table of contents
Introduction
2. Data size reduction of LXe detector
3. Summary and prospect

## Slide 3: μ→eγ search
We search for charged lepton flavor violating decay of muon, μ->eγ.
Prohibited in SM, detectable branching ratio in some BSM model
Main background is the accidental background.
Detector resolutions, especially energy resolution of γ-ray, are important to effectively distinguish the signal event from the accidental background.
Signal decay
Accidental background
Radiative muon decay
E=52.8MeV
back-to-back
coincident
Dominant background
E < 52.8MeV
not back-to-back
E<52.8MeV
not back-to-back
coincident
Signal
Background

## Slide 4: MEG II experiment
Upgrade of MEG experiment
μ+ stopping rate will be doubled
  3×107 μ/s → 7×107 μ/s
Detection efficiency will improve.
Resolutions of all detectors will become half.
New detector for background tagging will be introduced
Expected sensitivity: 4×10-14
One order of magnitude better than MEG
μ+ beam
e+
γ
Liquid Xe
γ-ray detector
e+ drift chamber
Gradient magnetic field
e+ timing counter
DAQ with muon beam
Engineering run
2017
2018

## Slide 5: LXe detector upgrade
MEG
2 inch PMT
γ
We will replace 216 2-inch PMTs on the γ-entrance face with 4092 12×12 mm2 MPPCs.
  Better granularity
    Better position resolution
  Better uniformity of scintillation readout
    Better energy resolution
  Less material of the γ-entrance face
    Better detection efficiency
We are upgrading LXe detector for MEG II to significantly improve the performance.
MEG II
12×12 mm2
MPPC
γ
inner
bottom
top
outer
lateral (US)
lateral (DS)

## Slide 6: Expected performance
Significant improvement of all resolutions and efficiency are expected.
 | MEG (measured) | MEG II (simulated)
Efficiency | 65% | 70%
Position | ~5 mm | ~2.5 mm
Energy | ~2% | 0.7 - 1.5%
Timing | 67 ps | 40 - 60 ps
Detector performance for signal γ-ray
MEG
log scale
MEG II
log scale
Imaging power improves

## Slide 7: Table of contents
Introduction
2. Data size reduction of LXe detector
3. Summary and prospect

## Slide 8
日本物理学会 (2016年秋季大会), 21aSE-1, 内山 雄祐 より

## Slide 9: Online data reduction
Several possibilities for data size reduction is being discussed.
  More efficient trigger.
  Online data reduction
  Additional software trigger
Online data reduction.
  Goal : 3M byte /event including all detector
  This study focus on the XEC whose number of channels increases by a factor of 5.
  Online data reduction algorithm has to be prepared not to affect the performance of the detector. -> Study by using MC simulation.
Detector
WaveDream board
DAQ concentrator board
Software trigger PC
DAQ backend PC
Offline cluster
Analog waveform
Compressed waveform
Online data reduction
Digitized waveform
Tape archive
Electronics
3rd level trigger
On site
Trigger concentrator board
1st level trigger
2nd level trigger

## Slide 10: Data reduction method No.1: Rebin of the waveform
Reduce the number of sampling point of the waveform.
Keep the maximum sampling speed only around the triggered pulse region.
  Necessary for precise timing information.
Waveform information of time region far from triggered is “rebined”.
  1024 points → 320 points (# of p.e. > 40 p.e.)
  1024 points -> 128 points (# of p.e. < 40 p.e.)
Also used in MEG.
triggered pulse
region
rebin region
V
μs
V
μs

## Slide 11: Data reduction method No.2: Online waveform clustering
Reduce the number of channel (i.e. granularity) of the readout.
Keep the granularity of the channels only around triggered gamma.
  MPPCs on the inner face are divided in a unit of 4×4 channels.
  If the pulse height is smaller than a given threshold, waveform from these 16 channels will be summed up and saved as one channel.
New for MEG II

## Slide 12: Performance of data reduction
Performance of the data reduction has been checked.
Data size
  Data size reduction by a factor of 6 has been achieved.
  0.54 Mbyte / event with data reduction. (+only 25% from MEG.)
  Sufficiently small to achieve the goal in MEG II (3 Mbyte /event).
Resolutions of reconstructed variables.
  Confirmed to be the same between w/ and w/o data reduction.
  Parameter for data reduction was set not to affect single gamma reconstruction.
 | w/o waveform clustering | w/ waveform clustering
w/o rebin | 1.00 | 
w/ rebin | 0.22 | 0.16
w/o data reduction
w/ data reduction
reconstructed energy (signal γ)
Data size after compression (arbitrary unit)
MeV

## Slide 13: Pileup identification
Pileup γ has to be “identified” and effect to the reconstructed variables has to be “eliminated”.
Two methods will be used for identification of pileup γ.
channel near pileup γ
channel near signal γ
  Number of photoelectron information.
  Search for a peak in light distribution.
  Timing information.
  Search for channels which have different timing.
pileup γ
signal γ
Difference of the timing exists.
multiple peaks found in light distribution

## Slide 14: Effect of data reduction to pileup identification
Pileup identification performance can be affected by data reduction.
  Information from channels with small photoelectrons is necessary to find low energy pileup.
The degradation of the performance exists but limited.
Efficiency | w/o waveform clustering | w/ waveform clustering
w/o rebin | 69.8% | 
w/ rebin | 69.8% | 65.0%
※Inefficiency to signal event (w/o pileup) : ~ 1% for all cases
signal γ
signal γ + pileup γ (Found)
signal γ + pileup γ (NOT found)
MeV
energy distribution (incl. pileup γ)

## Slide 15: Summary and prospect
The MEG II experiment searches for μ->eγ decay with the sensitivity of 4×10-14.
Total data size among the whole experiment might become a crucial issue for MEG II experiment.
Two methods have been developed for data size reduction of LXe detector, and sufficient performance has been confirmed by using MC simulation.
These methods will be tested in pre-engineering run at the end of 2017.
  Implementation to the DAQ software will be needed.
  Optimization of the parameters of the data reduction can be done with real data.

## Slide 16: backup

## Slide 17: Data reduction strategy
There are two kinds of information which can be reduced since they are not important for γ-ray reconstruction .
Time region far from triggered pulse.
Photo sensors which have the small number of photoelectrons.
V
μs

## Slide 18: aa
signal γ
signal γ + pileup γ (that are lost by the data reduction.)
signal γ + pileup γ (NOT found even w/o Data reduction)