## Slide 1: MEG II陽電子スペクトロメータ における機械学習を活用した ヒット再構成の改善 T Improving hit reconstruction for MEG II positron spectrometer using machine learning technique
内山 雄祐 on behalf of MEG II collaboration
日本物理学会2022年秋季大会 令和4年9月8日
8aA421-2

## Slide 2: MEG II in search of μ+ → e+γ
Search for μ+ → e+γ down to
6×10-14 (90% C.L. sensitivity)
B(μ+ → e+γ) < 4.2×10-13 @90% C.L.
(while 5.3×10-13 expected)
higher intensity muon beam
higher resolution everywhere
higher efficiency
An intensity frontier experiment
Upgraded from MEG experiment
To get definitive evidence for BSM
MEG result (2016)
UTokyo
KEK
Kobe Uni.
INFN Genoa
INFN Lecce
INFN Pavia
INFN Pisa
INFN Roma
PSI ETHZ
BINP
JINR
UC Irvine
~60 physicists

## Slide 3: MEG II
Started physics data taking in 2021!
  In this study, use 2021 data.
Cylindrical drift chamber (CDCH) (~1.6×10-3X0, σp~100 keV)
μ+
γ
e+
EPJ-C 78 (2018) 380
World’s most intense DC muon beam
  continuously emits (3 – 6) ×107 e+/s
  detected by a cylindrical drift chamber
Detector signals are read out as waveform
  by DRS4 waveform digitizer
  1024 points @ 1.2 GSPS

## Slide 4: Drift chamber: a nutshell
Signal formation
Charged particle generates primary ionization clusters discretely in gas
The ionized e-s drift to an anode wire and form avalanche near the wire
Reconstruction
Measure the timing of the 1st cluster
Draw a drift circle
Fit a track to the drift circles
+1450 V
vdrift ~ 3 cm/μs
Gas gain ~ 5×105
Primary ionization ~ 13 cluster/cm
t
t0
drift time
~ 300 ns
MEG II CDCH: an ultra low-mass chamber
Gas: He:iC4H10 = 90:10
Wires: 20 μm W anode + 40/50 μm Al cathode
  2 m long, 9 layers, 1152 readout cells in total
~7 mm
From a timing detector
To be measured

## Slide 5: Challenges
Detecting the 1st cluster signal is essential for the experiment
  The efficiency is directly connected to the e+ reconstruction efficiency, and thus, search sensitivity.
Two difficulties:
S/N
  The amplification process (gas gain) has large fluctuation obeying a Polya distribution. The 1st cluster signal can be very small.
Pileup
  Very high hit rate in MEG II: up to 1.7 MHz per cell, 35% occupancy in 250ns.
MC
Apply ML to the complicated waveform analysis.
mean: 9 mV
p(<5 mV) = 0.35
p(<2 mV) = 0.11
pileup hit
signal hit

## Slide 6: Current performance
A good momentum resolution achieved
  ~4 times better than that in MEG
Efficiency is not as good as designed
  In particular, at high beam intensity
  The goal: 70%
7aA442-2 大矢
2×107
3×107
4×107
5×107
date in 2021
σ=84 keV (core)
Gradually increased beam intensity
3×107 s-1

## Slide 7
Y. Uchiyama, JPS 2021 annual
Waveform from 8 wires × 2 ends

## Slide 8: Implementation
Training
Tensorflow 2.8 + Keras
in Python3.7
on Google Colab
with Tensor Processing Unit (TPU)
convert to ONNX format
Inference
ROOT based MEG II reconstruction framework
in C++17
ONNX Runtime C++ API
with CPU single thread (Xeon Gold 6138 2.0 GHz)
High flexibility × Easy maintenance
  Use one’s preferred package for model building & training.
  Use a common interface in C++ to use the trained model in inference/prediction.
  GPU/TPU in cloud are available for training, while only CPU (single thread) is available in the MEG II resource & framework.

## Slide 9: Noise estimation with 2D CNN autoencoder
True noise (target)
Estimated noise (output)
Noise + signal (input)

## Slide 10: Apply to 2021 data
Not better than the conventional analysis.
  Almost comparable performance with the best model
  but with > 10 times computation time (3.4 s/event)
Input (8, 512, 2)
⊖
CNN noise estimator
Standard wf analysis
Output: signal wf (8, 512, 2)
Track finder, pattern recognition
Standard wf analysis
Track finder, pattern recognition
ML detects almost same number of hits associated with trigger e+ with less fake hits.
However, final tracking efficiency is lower.
Track finder can reject fake hits. Better to input more hits.
Detected hit timing
Trigger counter time
Conventional
With ML
(μs)

## Slide 11: Extended model
Output1: signal wf
Output2: cluster timing
Transfer
learning
Track finder, pattern recognition
Input
cluster
detection
CNN noise estimator
⊖
Combine pulses detected by conventional & ML analyses
⊕
Pulse detection
Hit rec
Standard wf analysis

## Slide 12: Efficiency
Chart: 
| Conventional (before this study) | Conventional (tuned) | ML denoising | ML denoising + ML cluster timing | Conventinal + ML cluster timing | Conventinal + ML cluster timing (separable conv)
3×10^7 | 0.6 | 0.60753 | 0.5749 | 0.59498 | 0.65021 | 0.68536
5×10^7 | 0.45 | 0.49158 | 0.45 | 0.47446 | 0.56495 | 0.55516
23%
14%
Two different architectures (Discussed later)

## Slide 13: Computation time (ML)
Chart: second / event (Xeon Gold 6138 2.0 GHz)
| Conventional | ML denoising | ML cluster time | All separable conv
Waveform analysis | 0.23 | 3.37 | 6.62 | 1.85
5×107 s-1 data
  Inference speed is an issue!
  GPU/TPU is not available in MEG II resource & framework; only CPU (single thread).
  ~30 times slower (Unfeasible!)
  Can speedup with ‘separable convolution’
    Replacing all conv-layers with separable conv speeds up by factor 3.5 with comparable performance
    Feasible!
However, more practical problem is…

## Slide 14: Computation time (Total)
Chart: second / event
| Conventional | ML denoising | Conventional + ML cluster timing | Conventional + ML cluster timing (separable conv)
Waveform analysis | 0.23 | 3.37 | 6.62 | 1.85
Pattern recognition | 2.9 | 4.03 | 12.78 | 11.95
Track fitting | 0.75 | 1.02 | 1.61 | 1.45
5×107 s-1 data
Pattern recognition (track finding) is dominant part and becomes 4 times slower by adding more hit candidates
With current resource, it is not feasible to apply this to all events…

## Slide 15: Conclusions
Efficiency can be improved by feeding more hits to track finder
Even contaminated by fake or wrong timing hits Track finder is clever enough to find true track
ML model was extended (from denoising) to detecting cluster timing and the results are added to the results from conventional waveform analysis. → 23% higher efficiency.
Significant increase in computation time is problem
More by track finder than ML itself.
Next: developing global pattern recognition with ML to handle large number of hits in realistic computation time.

## Slide 16: Architecture

## Slide 17
⊗
filter kernels
patterns to be recognized
low-pass filter (moving average)
high-pass filter (differential)
Shaped (filtered) waveform = feature map
strongly ignited
=
Activation (relu) → nonlinearity

## Slide 18: channels
⊗
⊕
⊕
to the next layer
independent kernel (k points) for each channel
n channels
m channels
n×m kernels, n×m×k parameters in total
sum over channels